## Slide 1: March 19, 2013 Flight Indianapolis, IN
West winds
Two vertical profiles
Two upwind transects (beginning and end of flight)
Four downwind transects
Depth of boundary ~1100m (growth of ~50m over duration of flight)
Wind data was corrupted for portion of flight

## Slide 2: Flight Path
Notes: Left KLAF at approximately 11:49 EDT. After ascent on way to Indy, spiral descent for vertical profile 1 in the southwest corner of the city, followed by an upwind horizontal transect on the west side of the city. Survey across city completed followed by four horizontal downwind transects at four different levels (note: ascent above the boundary layer was done between the third and fourth downwind transect to determine height to do fourth transect). The second vertical profile is a transect across the southern part of the city, with half of an ascent due to already being at a high elevation from the downwind transects. After completion of both vertical profiles, one more upwind transect along the western edge of the city before returning to Purdue.

## Slide 3: CO2 Calibration

## Slide 4: CH4 Calibration

## Slide 5: Time Series Distribution
Spiral Descent
Vertical Profile 2
Notes: Spike in CO2 and CH4 downwind of Harding PP and Southside LF, respectively.

## Slide 6: Vertical Profile 1
Notes: Due to complications with the winds computer, the potential temperature during the spiral descent was lost. CO2, CH4 and H2O is not available during the ascent for vertical profile 1 due to calibrations. Boundary layer depth is approximately 1100 meters.

## Slide 7: Vertical Profile 2
Notes: Only half of of ascent available due to already high elevation after downwind transects. Boundary layer depth grew slightly, around 50m, by this time.

## Slide 8: Fight Path – CO2
Notes: Scale adjusted to 412 ppm to show enhancements across city. Spike in CO2 downwind of Harding PP approximately 420 ppm. Though the upwind transects overlap, differences in concentration can be seen from the beginning and end of the flight.

## Slide 9: CO2 Upwind Transect 1
Notes: Unknown CO2 source on very southwest side of city and generally higher concentrations on the southern half of the transect. This is puzzling, unsure if due to shallower boundary layer because the BL depth grew only ~50m. Possibly transport of CO2 from upwind sources?

## Slide 10: CO2 Upwind Transect 2
Notes: After growth of the boundary layer, concentrations on the second upwind transect are lower. However, the southern side of the transect still shows higher background values for CO2.

## Slide 11: CO2 Downwind Transects
Notes: Lower bounds of scale adjusted to approximately 403 ppm to show enhancements across transects (concentrations in section above the boundary layer are off the scale). The highest transect was flown in the transition zone (BL depth ~1100m)

## Slide 12: Flight Path – CH4
Notes: Scale adjusted to approximately 1.9 ppm to better show enhancements across city. Increased CH4 is seen downwind of Southside Landfill. Note the increased concentration on the NW side of the city while returning to Purdue. A similar enhancement was seen in the 3/14/2013 flight and is likely due to hog/pig farms in Boone County.

## Slide 13: CH4 Upwind Transect 1
Notes: Similar to CO2, upwind CH4 concentrations are higher in the upwind transect at the beginning (seen here) of the flight compared to the second upwind transect. This is puzzling, unsure if due to shallower boundary layer because the BL depth grew only ~50m. Possibly transport of CH4 from upwind sources?

## Slide 14: CH4 Upwind Transect 2

## Slide 15: CH4 Downwind Transects
Notes: Lower bound scaled to approximately 1.91 ppm to show enhancements across transects (concentrations in section above the boundary layer are off the scale).